## Slide 1: Toward Trusted and Swift UAV Communication: ISAC-Enabled Dual Identity Mapping
Cui, Y., Feng, Z., Zhang, Q., Wei, Z., Xu, C., Zhang, P.
IEEE Wireless Communication 2023
2024.10.08.
Summarized by, Sangwi Kang | swkang@mmlab.snu.ac.kr

## Slide 2: Outline
Introduction
ISAC : Integrated Sensing and Communication
ISAC-Enabled Dual Identity Solution
Solution Structure
Scenario and Advantage
Open Challenges
Conclusion

## Slide 3: Introduction
UAV networks are expected to be a promising carrier for wireless intelligent communication and 6G network
However, UAV networks implicates security and efficiency issues
  Simplified verification, removing repetitive feedbacks
To ensure trusted and swift UAV networks, the UAV should utilize both physical and digital identity
And the ISAC (Integrated Sensing and Communication) can utilize both of them, by achieving S&C functionalities together
This paper presents ISAC-enabled dual identity solution for trusted and swift UAV communication
Sensing & Communication

## Slide 4: ISAC : Integrated Sensing and Communication
The IMT-2023 vision document was drafted on June 22, 2023, and lays out the future vision for 6G communications
ISAC is one of the main scenarios for IMT-2030
Co-existence of S&C (sensing & communication) to Integrated S&C
 Network as Sensor
Trustworthy Physical Interfaces, barkhausen institut
Sixth-Generation Networks and Integrated Sensing and Communications, ETRI Electronics and Telecommunications Trends, 38-6, Dec, 2023

## Slide 5: ISAC-Enabled Dual Identity Solution > Overview
Purpose
  Removing the tedious communication feedback
  Removing beam management latency
  Ensuring communication security
Method
  Using the benefits of ISAC technology
  Utilize Rich information of the signal
  And the accurate physical features of the echo
Structure
  Feature : Physical identity, digital identity
  Domain : AD (Auditory Domain), VD (Visual Domain)
  Modules : Identity production / mapping / management / authentication
 Get accurate UAV physical-digital identity mapping
(Necessary but repetitive process)

## Slide 6: ISAC-Enabled Dual Identity Solution > Terminology
AD : Auditory Domain
  Just catch the signal passively
  Obtain the information
VD : Visual Domain
  Actively sends the signals or use features and sense the environment
DID : Digital Identity
  Digital identity for authentication process
  IP/MAC address, unique keys, RF fingerprint, etc.
  Only obtained from AD
PID : Physical Identity
  The physical properties of a UAV node
  Wing type, location, velocity, distance, etc.
  Both of the AD and VD information can be used

## Slide 7: Solution Structure > Overview

## Slide 8: Solution Structure > Identity Production Module
Receive information from AD & VD
Based on the echoes from the ISAC signal, the module can estimate PID
  Matched-filtering of Doppler-shifted echo
  Micro-Doppler frequency
Physical attributes are dynamically weighted  Valid for distinguishing the all types of UAVs
DIDs are only obtained from AD

## Slide 9: Solution Structure > Identity Mapping Module
Receive PID & DID from Identity Production Module
Calculate the similarity between PID & DID and perform ID matching
Matching cost
  th identity of VD
  th identity of AD
Matching cost optimization
  Hungarian algorithm
  Vampire bat optimizer

## Slide 10: Solution Structure > Identity Management Module
In dynamic environment, it is hard to ensure the accuracy of matching result
Before the next AD information arrives,
  Current PIDs from VD
  Previous PID & DID from AD
The Identity Management Module estimates the current AD information with previous AD information
  NN or classical Kalman filter
  Joint probabilistic data association filter
  Multiple hypothesis tracking

## Slide 11: Solution Structure > Identity Authentication Module
Identity Authentication Module provides the trusted local and global identity
Authentication Roles
  Requestor
  Witness
  Certifier
Performing the minimum mean-square error for Witness and Requestor
Maximum common sub-graph also can be used to detect the malicious node
R
W
W
W
C
(R ID)
(R ID)
(R ID)
Calculate Error
(, , )

## Slide 12: Scenario and Advantage > Low-Latency Beam Management
It is essential that the BSs quickly find the optimal beam direction for the UAV
By DID to PID mapping, the BSs can perform a rapid beam alignment

## Slide 13: Scenario and Advantage > Low-Latency Beam Management
Reduced communication delay about 4.6ms
The echo signal processing delay is negligible at about 1ms

## Slide 14: Scenario and Advantage > Swift Transmission of Emergency Messages
Traditional broadcasting alert system can cause issues on unintended nodes
By PID to DID mapping, the UAV can deliver the alert to a specific DID

## Slide 15: Scenario and Advantage > Trusted Networking Under Sybil Attack
Sybil Attack
  A single entity creates multiple fake identities on a network
  Use fake identities to manipulate consensus, distort certain information, etc.

## Slide 16: Scenario and Advantage > Trusted Networking Under Sybil Attack
By PIDs from VD, we know the existence of malicious node
However, we don’t know which one is the actual malicious one
By PID to DID mapping, the UAV can easily distinguish the malicious node
?
?
?
Deviation
Deviation
Deviation
Deviation

## Slide 17: Scenario and Advantage > Trusted Networking Under Sybil Attack
Achieved higher precision for various mobility settings and network density

## Slide 18: Conclusion
ISAC technology is essential for UAV networks and 6G communication
ISAC-Enabled Dual Identity Solution improves the reliability and security of the UAV network
Specifically, the solution is effective for managing beam alignment and emergency message delivery
It also raises authentication level for the entire UAV network
The authors showed the usefulness of ISAC for UAV networks, and it was meaningful point to cover form a security and authentication perspective
However, ISAC can be vulnerable, so it’s important to consider the security of the ISAC itself