## Slide 1: A System to Detect Forged-Origin BGP Hijacks
mhkang 2024-08-20
NSDI ‘24

## Slide 2: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate

## Slide 3: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate

## Slide 4: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate
Reject! It’s RPKI-Invalid!
Reject! It’s RPKI-Invalid!

## Slide 5: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate

## Slide 6: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate

## Slide 7: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate

## Slide 8: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate

## Slide 9: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate

## Slide 10: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate
No such link exists! (between AS 6 and AS 9)

## Slide 11: Forged-origin BGP hijack
a BGP hijack attack
  an attacker announces forged AS paths towards a victim prefix by prepending the victim’s origin AS number to make them appear legitimate
Detecting forged-origin BGP hijacks can be reduced to identifying fake links between ASes!
No such link exists! (between AS 6 and AS 9)

## Slide 12: The challenge of identifying fake links
There are many new AS links every day but no simple property that tells whether they are real or fake
  166 new AS links every day (median) and the vast majority are likely legitimate
?

## Slide 13: Limitations of existing approaches
Existing link prediction approaches [1, 2] does not perform well on detecting fake links
  not suitable capture the characteristics of hierarchical AS topology
ARTEMIS [3] can be used to detect forged-origin hijacks but it is self-operated
  only capable of detecting hijacks targeting the AS deploying it
[1] Dimitrios Panteleimon Giakatos, Sofia Kostoglou, Pavlos Sermpezis, and Athena Vakali. Benchmarking Graph Neural Networks for Internet Routing Data, 2022.
[2] Muhan Zhang and Yixin Chen. Link prediction based on graph neural networks. In Advances in Neural Information Processing Systems, 2018.

## Slide 14: Requirements of a forged-origin detection system
must be fast and accept real-time and historical queries
must be accurate, both for pinpointing actual hijacks and avoiding triggering false alarms
must be robust against missing, inaccurate and polluted data
must be accurate in all attack and peering scenarios

## Slide 15: DFOH: A System to Detect Forged-Origin BGP Hijacks

## Slide 16: DFOH inference pipeline
Finding New Links
Computing Features
Inferring Hijacks

## Slide 17: Finding New Links
Finding New Links
Computing Features
Inferring Hijacks
date | d-k | … | d | d+1
BGP update |  |  |  | 
RIB |  |  |  | 
CAIDA |  |  |  | 

## Slide 18: Finding New Links
Finding New Links
Computing Features
Inferring Hijacks
date | d-k | … | d | d+1
BGP update |  |  |  | 
RIB |  |  |  | 
CAIDA |  |  |  | 
Gd,k
AS topology graph

## Slide 19: Finding New Links
Finding New Links
Computing Features
Inferring Hijacks
date | d-k | … | d | d+1
BGP update |  |  |  | 
RIB |  |  |  | 
CAIDA |  |  |  | 
AS links
Gd,k
AS topology graph

## Slide 20: DFOH inference pipeline
Finding New Links
Computing Features
Inferring Hijacks
Builds an AS topology graph Gd,k using the AS paths from
- BGP updates collected from 287 BGP vantage points (from the day d-k to the day d)
- RIB of 287 BGP vantage points (at the day d)
- CAIDA datasets (at the day d)
Collects the BGP updates from the 287 BGP vantage points observed at the day d+1
extracts AS paths and checks whether an AS link in the AS paths in the AS topology graph Gd,k

## Slide 21: Finding New Links
Finding New Links
Computing Features
Inferring Hijacks
date | d-k | … | d | d+1
BGP update |  |  |  | 
RIB |  |  |  | 
CAIDA |  |  |  | 
AS links
?
Gd,k
AS topology graph

## Slide 22: Computing Features
Finding New Links
Computing Features
Inferring Hijacks

## Slide 23: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
1. Topological features
- quantify the change induced by a new link on the AS topology

## Slide 24: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- quantify the change induced by a new link on the AS topology
- a total of 11 topological features that can be divided into four categories
1. Topological features

## Slide 25: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- use public peering information to identify peering characteristics
- Intuitively, two ASes that exhibit similar peering characteristics have a higher chance to peer
2. Peeringdb Features

## Slide 26: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- use public peering information to identify peering characteristics
- Intuitively, two ASes that exhibit similar peering characteristics have a higher chance to peer
2. Peeringdb Features

## Slide 27: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- use public peering information to identify peering characteristics
- Intuitively, two ASes that exhibit similar peering characteristics have a higher chance to peer
2. Peeringdb Features

## Slide 28: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- use public peering information to identify peering characteristics
- Intuitively, two ASes that exhibit similar peering characteristics have a higher chance to peer
2. Peeringdb Features

## Slide 29: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- use public peering information to identify peering characteristics
- Intuitively, two ASes that exhibit similar peering characteristics have a higher chance to peer
2. Peeringdb Features
compares the peering information of the neighbors
→ protect against adversarial input & mitigate missing peering information

## Slide 30: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- examine the AS paths that include the new link and identifies suspicious sequence of ASes
3. AS-path patterns

## Slide 31: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- examine the AS paths that include the new link to identify suspicious sequence of ASes
3. AS-path patterns

## Slide 32: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- examine the AS paths that include the new link to identify suspicious sequence of ASes
3. AS-path patterns

## Slide 33: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- examine the AS paths that include the new link to identify suspicious sequence of ASes
3. AS-path patterns

## Slide 34: Computing Features
Finding New Links
Computing Features
Inferring Hijacks
- checks whether an AS link is observed in both directions
4. Bidirectionality

## Slide 35: Inferring Hijacks
Finding New Links
Computing Features
Inferring Hijacks

## Slide 36: Inferring Hijacks
Finding New Links
Computing Features
Inferring Hijacks

## Slide 37: Inferring Hijacks
Finding New Links
Computing Features
Inferring Hijacks

## Slide 38: Inferring Hijacks
Finding New Links
Computing Features
Inferring Hijacks

## Slide 39: Inferring Hijacks
Finding New Links
Computing Features
Inferring Hijacks

## Slide 40: Inferring Hijacks
Finding New Links
Computing Features
Inferring Hijacks

## Slide 41: Evaluation
Evaluated the accuracy of DFOH
  classify 9K existing links → correctly detects 8,181 forged-origin hijacks (TPR = 0.909)
  classify 9K nonexistent links → incorrectly inferred 171 legitimate links as forged-origin hijakcs (FPR = 0.019)

## Slide 42: Evaluation
Sample 100 links for every attack scenario

## Slide 43: Evaluation
Sample 100 links for every attack scenario
The minimum TPR is 0.73

## Slide 44: Evaluation
Sample 100 links for every attack scenario
The minimum TPR is 0.73

## Slide 45: Evaluation

## Slide 46: Evaluation
Each day, 180 new links are observed, but DFOH only classifies 17.5 of them are suspicious

## Slide 47: Conclusion
Identify the key factors to consider when designing a forged-origin hijack detection system
Design and present DFOH which quickly and accurately detects any forged-origin hijacks on the whole Internet
Show the evaluation of DFOH on synthetic and real data demonstrating that DFOH is effective in defending against forged-origin hijacks

## Slide 48: Thank you

## Slide 49: Topological Feature

## Slide 50: Topological Feature